## Slide 1: PROJECT WHIPTAIL
Secured IT/OT Integration
MAY
2021

## Slide 2: AGENDA
01
Introduction
02
Schedule
03
Original Network Design
04
Penetration Test
05
Risk Assessment
06
Countermeasures
07
Honeypot
08
Improved Network Design
09
Questions

## Slide 3: INTRODUCTION
Mink Jo
Schedule
Countermeasures
Gary Khodayari
Risk Assessment
Penetration Test
Michael Klym
Network Design
Installation and Configuration
Security Appliances

## Slide 4: INTRODUCTION
Create an IACS network demonstrating vulnerabilities
Conduct risk assessments following ISA/IEC 62443 guidelines
- Identify assets
- Prioritize countermeasures based on Security Level Targets
Upgrade network and add security appliances
- Firewalls
- SIEM system
- Honeypot
Create the final technical report
Scope

## Slide 5: SCHEDULE
WBS (WORK BREAKDOWN STRUCTURE)

## Slide 6
PROJECT SCHEDULE NETWORK DIAGRAM

## Slide 7: ORIGINAL NETWORK DESIGN
Simulate ICS Environment
Fully Virtualized
Low System Requirements
Requirements

## Slide 8: ORIGINAL NETWORK DESIGN
Simplification
Inspired By Pascal Ackerman’s ICS Virtual Test Network (Industrial Cybersecurity)
Remove Redundant Equipment
Retain Core Zones
Reduce Hardware Requirements

## Slide 9: ORIGINAL NETWORK DESIGN
VMware Networking
Virtual Network Editor
Create Zone Networks
Assign Subnets
Static IPv4 Addressing
Public Network NAT Configuration
  VMware acts as Default Gateway
IT & OT Networks
  Host-only
  No Connected Host Virtual Adapter

## Slide 10: ORIGINAL NETWORK DESIGN
Installing Machines
Publicly Available Images
Pre-built Where Possible
Allocate Resources Efficiently
Host Requirements
  4 CPU Cores
  8.5 GB RAM (plus overhead)
  ~100 GB Storage (table shows maximums)

## Slide 11: PENETRATION TEST
Testing the limits of our design

## Slide 12: SUMMARY
We sets up a website carrying the payload
Victim downloaded and executed the payload
We tunneled HTTPS traffic through the victim's computer to access the firewall/router configuration and enabled SSH and RDP port forwarding
We used RDP connection to modify PLC program

## Slide 13: LOCKHEED MARTIN CYBER KILL CHAIN
Developed By Lockheed Martin
A Defense Model For Identification And Prevention Of Cyber Intrusions Activity.

## Slide 14: RECONNAISSANCE, WEAPONIZATION & DELIVERY
Social Engineering is the most common initiation for cyber attacks
Social platforms like LinkedIn make it easy to research people and companies
Choose a payload based on the access you have and the tools you need
There are many exploitation options for older systems that exist in IACS environments
Free software is available for social engineering (KingPhisher, SET, and BlackEye)
Humans Can Be An Organization’s Strongest Suit Or The Weakest Link

## Slide 15
Payload
Kali public IP and listening port
Payload format
Path

## Slide 17: EXPLOITATION & INSTALLATION
Possible lateral movement from inside computer
Abusing the trust from inside devices
The Payload Executed By The Employee Gives Us Full Access

## Slide 18
Listening device’s public IP
Listening port
Router public IP and port
Success

## Slide 19: COMMAND & CONTROL
Setup for action phase
Scan the network
Exfiltrate hashes and password
Find a path
We Have To Setup For Our Action Phase And Get To Know The Network

## Slide 20
Privilege escalation
IP on network #1
Gateway on network #1
IP on network #2
Network #2 has no gateway

## Slide 21
Administrator password
Windows
NTLM
Attack mode: dictionary straight
Save file
Hashes file
Dictionary file

## Slide 22
Gateway router/firewall has its HTTP and HTTPS ports open
Modbus devices on the second network

## Slide 23
Enabling RDP through modifying windows registries

## Slide 24
The IP and port of what we want to mirror
The port on the kali machine we are mirroring the traffic on
Listening public IP and port
Mirroring session created

## Slide 25
Open the mirrored port on localhost on Kali

## Slide 27
pfSense reminds you to change your default password

## Slide 29: ACTIONS ON OBJECTIVES
With full control over the network and devices inside of it we can do whatever we want
Denial of Service
Physical Disasters
Data Exfiltration
Ransom
With A Clear Path In Mind, Now We Can Achieve Our Objective

## Slide 31: CLEAN UP
Clear memory
Clear used files
Clear logging data
Clear application data
Since The Network Doesn’t Have A SIEM And Logging Server, Wiping Out The Victim System Is Enough

## Slide 32: RISK ASSESSMENT
ISA/IEC 62443 Based
Identify Assets
Create Zones and Conduits
Understand Foundational Requirements
Choose Security Levels
Apply Design Principles
(Refer to Extensive Report)

## Slide 33: UPDATING OUR NETWORK DESIGN

## Slide 34: COUNTERMEASURES
pfSense Firewall
FreeBSD based firewall
Two firewalls
- IDMZ firewall
- Gateway firewall
Domain Controller
Windows Server 2019
Account administration
- group policies
- domain user accounts
System management controls
DNS resolver
Security Onion SIEM
Kibana - Dashboard
Suricata – detect threats and generate alerts
Wazuh security monitoring as a HIDS
Osquery – request real-time information and reporting from the network system

## Slide 35: COUNTERMEASURES
Honeypot - Conpot
ICS/SCADA honeypot
Light weight honeypot using Python script
Installation and Configuration
- Kubuntu
- Custom Start Script
Conpot
Exploit

## Slide 36: COUNTERMEASURES
Splunk SIEM
Software platform to search, analyze and visualize the machine-generated data gathered from the devices
Sorts out the logs using indexes
Generates alerts

## Slide 37: COUNTERMEASURES
Conpot – Splunk Simulation

## Slide 38: COUNTERMEASURES
Conpot – Splunk Simulation

## Slide 39: IMPROVED NETWORK DESIGN
Builds on the Original
Learns from the Assessment
Increases Network Visibility
Upgrades

## Slide 40: IMPROVED NETWORK DESIGN
Separating Equipment
Adding Zones
Increasing Segmentation
Limiting Traffic Paths
Defense in Depth
5 Areas

## Slide 41: IMPROVED NETWORK DESIGN
Firewalls
Stateful Firewall Operation
  Traffic is filtered on port of ingress
  Connection tables verify return traffic
Certain Traffic Permitted on Specific Ports
  (And in specific directions)
Rules…
  Enterprise Zone may not reach Industrial Zone
  Enterprise and Industrial Zones may Connect to IDMZ
  IDMZ may not Initiate Industrial Zone Connections
  Industrial Zone has no WAN Access
  …and more

## Slide 42: IMPROVED NETWORK DESIGN
Domain Controller
Windows Server 2019
Domain Server Role
  Enables Domain User Accounts / Groups
  Group Policy Affects all Domain Joined Systems
DNS Server Role
  All DNS Requests in the Network are Visible
  (Domain Name System)

## Slide 43: IMPROVED NETWORK DESIGN
Security Onion
Threat Hunting
Network Monitoring
Log Management
Wazuh Agents
  HIDS for Windows, macOS, Linux OSes
  Event and Security Logs sent back to Security Onion
Osquery
  Custom SQL-like Queries of Client Machines
  Request Real-Time Information from ‘Fleet’ Systems
Osquery ‘Fleet’ Devices
Kibana Network Dashboard

## Slide 44: IMPROVED NETWORK DESIGN
Honeypot
Conpot IACS Honeypot
Looks Valuable
Provides Security Team with Attacker Information
Alerting Mechanism when Coupled with Splunk

## Slide 45: IMPROVED NETWORK DESIGN
Installing Machines
Host Requirements
  8 CPU Cores
  27 GB RAM (plus overhead)
  ~200 GB Storage (table shows maximums)

## Slide 46: FINAL RISK ASSESSMENT
Security is not a Destination
Continual Improvement is Necessary
Workflow
  Implement Design
  Test Network
  Assess Risks
  Decide if Risk is Tolerable or Not
  Design Countermeasures
  Repeat
Reassessment

## Slide 47: SUMMARY
Build initial network system
Perform penetration test
Perform risk assessment
Apply countermeasures
Upgrade network system

## Slide 48: QUESTIONS

## Slide 49: THANK YOU!
Michael Klym Gary Khodayari Mink Jo